The information below is based on the Hall D concept drawings of 2002, Accelerator drawing from 2002 timeframe, GlueX equipment slide from 2005, and Hall D Concept drawings of July 2005:

| Beam Line Element | Incremental Distance (m) | Distance from Point of Tangency (m) | Beam Height Above Finish Floor (AFF) | Coordinates | Comments |
| --- | --- | --- | --- | --- | --- |
| Point of tangency | 0 | 0 |  |  | Approximately center of Bldg 39, E. Arc service bldg |
| Start of beam line incline | 22.42 | 22.42 |  |  |  |
| End of beam line incline | 38 | 60.42 |  |  |  |
| Radiator | 23.58 | 84 |  |  | Request to increase dimension by 10 m to 94 for 8 deg bends. Where is the increase? |
| Tagger Magnet (west end) | 3 | 87 | 1.5 m | 288.21379, 104.70001 | Request to increase beam height AFF. |
| Collimator enclosure (interior west wall) | 74.35 | 161.35 |  |  |  |
| Collimator (west end) | .65 | 162 |  |  | Need 75 m minimum from beginning of tagger magnet to collimator |
| East end of collimator enclosure / Hall D (interior west wall) | 11.35 | 173.35 |  |  |  |
| GlueX solenoid | 10 | 183.35 |  |  |  |
| End of Hall D (interior east wall) | 20 | 203.35 |  |  |  |
| Photon Beam Dump (east end) | 5.4 | 208.75 |  |  |  |
| Fence | 77 | 285.75 |  |  | Need 66 m from center of Hall D to fence for radiation protection. |
| Canon Blvd (west side) | 26 | 311.75 |  |  |  |
| Additional Elements |  |  |  |  |  |
| Permanent Magnets |  |  |  |  |  |
| Electron Beam Dump |  |  |  |  |  |