PS design progress since May 2008

H.Hakobyan(YERPHI)

- - an appropriate dipole magnet is found in BNL. Bmax=1.85T, Leff=1.83m, Pole width=0.6m

- - then a final design is done, including  the choice of analyzed energy range: 6 to 12 GeV, hodoscopes: 24x6 configuration in first layer of positron and electron arms and 4x6 configuration in the backward layer.

- - details of the tagger and PS intercalibration, endpoint energy calibration for PS energy sca le, influence of multiple scattering,  background conditions are considered.

- electronic scheme is elaborated in agreement with the electronic design stream of Hall D.

- - the work is done in cooperation with R.Jones, J.Stewart, F.Barboza  and A.Somov