## Slide 1: TAGGER MAGNET DESIGN
Presented by Tim Whitlatch

## Slide 2: Tagger Area
North Wall
Shielding
Beamline encasement to Hall D
AC ducts
Radiator
Vacuum Chamber
Quad
Electron dump
Truck ramp entrance
Permanent Magnet
Tagger Magnet
Photon Beamline
Beam Current Monitor
Vacuum gages and pump

## Slide 3: Tagger Components
Tagger support stands
Hodoscope frame attach points
Tagger strong back
Vacuum Chamber supports
Magnet steel
Vacuum chamber
Coils
Preloaded threaded rod

## Slide 4: Tagger Cross-Section
Adjustment cartridges use wedge type for vertical
Sliders for X-Z
+/- 1cm horizontal plane adjustment
+/-9mm vertical adjustment (standard part)
Each piece under 25 tons
Provision for porta-power for alignment
Vacuum chamber and pole form integral vacuum space
Adjustment cartridges

## Slide 5: Magnet Cross-Section from Yang’s TOSCA (early version)
Rowgoski contour all edges
Gap machined to within ±.004 inches
All steel 1006 annealed

## Slide 6: Vacuum Chamber Support
Window opening Support rods
Support tubes
Vacuum Chamber
Window opening 45mm x 11.2 m
O-ring Support rods

## Slide 7: Vacuum Chamber
Stiffening ribs 1 inch plate
Skin, 0.25 inch plate
O-ring groove along entire edge, top and bottom
Photon beam tube
12GeV electron beam exit opening
Additional port for mag field probes both ends (location TBD due to synchrotron radiation)
Add vacuum pumping port (not shown)
Beam

## Slide 8: O-ring Groove (3/8)
Port for mag field probes both ends
Thin window
Thicker flange for radius of o-ring groove
Beam tube
Generous Radii (1.3 in) for better sealing
Support features
Add pumping port
Beam

## Slide 9: Vacuum Seal Details
Coil
Vacuum Chamber back wall
O-ring
Pole tip
Lower pole
Upper pole
Support rod
30mm gap

## Slide 10: Vacuum Chamber Exit
25 x 4.5 cm 12GeV electron beam opening
2.5 cm thick flange
45mm x 11.2 m window opening (thin window)

## Slide 11: Coils
6.509 m
548 mm
Magnet Coils
  12 by 7 cu/epoxy matrix.
  11 mm sq cu
  7 mm water path
  1.5 T 220A 105V
  1.8 T 366A 200V

## Slide 12: Coils Connections
Magnet Coils Electrical
  Series
  1.8 T 366A 200V
  0.52 ohms
Klixons and electrical flag connections needed
Tubes brazed together to form series circuit
Plexiglass shield for safety
Magnet Coils Cooling
  28 parallel circuits LCW
  34GPM
  8°C∆T
  6.5 ft/sec

## Slide 13: Tagger Support
I-beam strongback
3-point adjustment
±9mm vertical adjustment
±1cm x-y adjustment
Vacuum chamber support
Stands grouted in place after alignment
Final magnet alignment after install
Strongback
Vacuum Chamber supports
Base stands
Adjustment cartridges
Hodoscope attach points

## Slide 14: Tagger Alignment
Use optical means to determine relation between pole edges and fiducials on each slab within 50 microns
Laser tracking fiducial targets on tagger magnet to position relative to monuments within 40 microns
Targets visible after install on upstream end
Optically sight pole edges

## Slide 15: Status of 3D Model
Magnet mostly modeled (needs coil support features)
Coil attach and layout needs to be complete
Vacuum chamber needs flange and window attach features
Support stands and adjustment mechanisms need more detail
Need to add jacking and alignment features to magnet steel

## Slide 16: What Needs to be done?
Finalize analysis on vacuum chamber and stand
Finalize hodoscope attachment
Analyze magnet support structure
Complete coil support design
Complete coil electrical/cooling design
Finalize tagger spec and SOW
Produce complete design drawings for tagger components
Procure/manufacture components
Detail installation procedure
Write analysis tech note (pressure system and structural)
Perform ES&H detailed analysis
Develop detailed plan for mapping
Thin window design
Look at ¼” o-ring