## Slide 1: Start program
Start
Start Time Duration Counter.
Prompt user to save data in file.
Allow user to choose run mode.
If temperature is above a danger level, turn off heater and prevent heating for remainder of run.
Automatic
Manual
Heater On
Heater Off

## Slide 2: Automatic Mode
Automatic
Heat and Cool
Maintain Temperature Range
If temperature is below a certain level:
Turn on heater.
Turn on heater power light.
Heat to target temperature.
At target temperature:
Turn off heater and prevent heating for remainder of run.
Turn off heater power light.
While heating, if temperature spread between coldest and hottest thermistors is less than or equal to 2.778 °C (5°F):
> Target temperature is 71.111 °C (160 °F).
Otherwise:
> Target temperature is 73.889 °C (165 °F).
When temperature drops to a certain level:
> Stop recording data.
1. If temperature is below a lower bound:
Turn on heater.
Turn on heater power light.
2. At upper bound:
Turn off heater.
Turn off heater power light.
While heating, if temperature spread between coldest and hottest thermistors is less than or equal to 2.778 °C (5°F):
> Target temperature is 71.111 °C (160 °F).
Otherwise:
> Target temperature is 73.889 °C (165 °F).
Repeat steps 1 and 2 as temperature rises and falls.